## Slide 1: CS4101 嵌入式系統概論 Task Scheduling
Prof. Chung-Ta King
Department of Computer Science
National Tsing Hua University, Taiwan
(Materials from Using the FreeRTOS Real Time Kernel, Richard Barry,
Study of an Operating System: FreeRTOS, Nicolas Melot, and
http://www.eecs.umich.edu/eecs/courses/eecs373/Lec/RTOS2.pptx)

## Slide 2: Outline
Task scheduler of FreeRTOS
  Priority and ticks
  Delaying a task
  Suspending and resuming a task
  Idle task hook
  Changing priority
Representative RT scheduling algorithms

## Slide 3: Scheduler of FreeRTOS
Task scheduling: decide which task in “Ready” state is to be run at a given time
RTOS scheduler is started by calling
  void vTaskStartScheduler(void);
  RTOS kernel now has control over which tasks are executed and when (Arduino invokes it automatically)
An Idle task is automatically created by scheduler when vTaskStartScheduler() is called
  Because CPU always needs something to execute  must always have one task that can enter Running state
  The idle task has the lowest priority (priority 0) to never prevent a higher priority task from running

## Slide 4: Task Priority
FreeRTOS only uses the priorities of tasks to decide which task to run next
The uxPriority parameter of xTaskCreate() assigns an initial priority to the task being created
  Can be changed using vTaskPrioritySet()
  Low numeric priority values denote low priority tasks
Scheduler always selects the highest priority task that is able to run
  When more than one task of the same priority is able to run, the scheduler uses round-robin

## Slide 5: Ticks
To select the next task to run, the scheduler has to be executed periodically
  By a periodic interrupt called the tick interrupt
FreeRTOS API calls always specify time in tick interrupts (or just ‘ticks’)
‘Tick count’ is the total number of tick interrupts that have occurred since the scheduler was started

## Slide 6: Sample Code for Task Priority
static const char *pcTextForTask1 = “T1 running\r\n”;
static const char *pcTextForTask2 = “T2 running\t\n”;
void setup() {
/* Create the first task at priority 1. */
xTaskCreate(vTaskFunction, "Task 1", 1000,
(void*)pcTextForTask1, 1, NULL);
/* Create the second task at priority 2. */
xTaskCreate(vTaskFunction, "Task 2", 1000,
(void*)pcTextForTask2, 2, NULL);
/* Start scheduler so the tasks start executing. */
vTaskStartScheduler();
return 0;
}

## Slide 7: Running Multiple Periodic Tasks
It is inconvenient to run multiple periodic jobs using a single Arduino loop, e.g.
  Measure the light using the photoresistor at 1 Hz
  Measure the sound intensity using microphone at 2.5 Hz
  Measure the distance of an object using the ultrasonic sensor at 0.4 Hz
Even if we run each job in a FreeRTOS task, we still need a way to schedule the tasks at specified time
Use blocked state with vTaskDelay()

## Slide 8: Delaying a Task
void vTaskDelay(const TickType_t xTicksToDelay)
  Places the calling task into the Blocked state for a fixed number of tick interrupts
  While in the Blocked state, the task will not use any processing time
  Note: Frequency of the periodic task depends on the path of the code, as well as other tasks and interrupt activities
void vTaskFunction(void * pvParameters) {
const TickType_t xDelay = 500/portTICK_PERIOD_MS;
for( ;; ) {
vToggleLED(); // toggle LED
vTaskDelay(xDelay); // Block for 500 ms
}
}
duration of a tick in msec
Notes: portTICK_PERIOD_MS: duration of a tick in msec
tick interrupt frequency is configured by the application-defined configTICK_RATE_HZ compile time configuration constant within FreeRTOSConfig.h

## Slide 9: Delaying a Task
void vTaskDelayUntil(TickType_t *pxPreviousWakeTime, const TickType_t xTimeIncrement);
  Delay a task until a specified time  to ensure a constant execution frequency
    vTaskDelay() specifies a time at which the task wishes to unblock relative to the time at which vTaskDelay() is called
    vTaskDelayUntil() specifies an absolute time to unblock the task
  pxPreviousWakeTime: the time that task last left Blocked state
    This time is used as a reference point to calculate the time at which the task should next leave the Blocked state
  xTimeIncrement: frequency of the periodic task in ‘ticks’
  vTaskDelayUntil() will return immediately without blocking if the specified wake time is already in the past

## Slide 10: Sample Code for Periodic Tasks
void vTaskFunction(void * pvParameters){
// Perform an action every 10 ticks
TickType_t xLastWakeTime;
const TickType_t xFrequency = 10;
// Initialize xLastWakeTime with the current time.
xLastWakeTime = xTaskGetTickCount();
for( ;; )
{
// Wait for the next period.
vTaskDelayUntil(&xLastWakeTime, xFrequency);
// Perform action here.
}
}
Notes: volatile TickType_t xTaskGetTickCount( void );
Returns: The count of ticks since vTaskStartScheduler was called.

## Slide 11: Software Timer
A software timer (or just a ‘timer’) allows a function to be executed at a set time in the future.
  The function executed by the timer is called the timer’s callback function. The time between a timer being started, and its callback function being executed, is called the timer’s period. Put simply, the timer’s callback function is executed when the timer’s period expires.
To make the FreeRTOS software timer API available in an application, simply:
  Add the FreeRTOS/Source/timers.c source file to your project, and
  Define the constants detailed in the table below in the applications FreeRTOSConfig.h header file.
Notes: xTimerCreate, xTimerCreateStatic, xTimerIsTimerActive, pvTimerGetTimerID pcTimerGetName vTimerSetReloadMode xTimerStart xTimerStop xTimerChangePeriod xTimerDelete

## Slide 12: Suspending and Resuming a Task
void vTaskSuspend(TaskHandle_t xTaskToSuspend)
  Suspend any task
  Task will never get any CPU processing time, no matter what its priority
  Calls to vTaskSuspend() are not accumulative, i.e. calling vTaskSuspend () twice on the same task still only requires one call to vTaskResume () to ready the suspended task
void vTaskResume(TaskHandle_t xTaskToResume)
  Resumes a suspended task
  A task that has been suspended by one or more calls to vTaskSuspend () will be made available for running again by a single call to vTaskResume ()

## Slide 13: Sample Code for Suspending a Task
void vTaskMaster(void) {
TaskHandle_t xHandle;
// Create a slave task, storing the handle xTaskCreate(vTaskSlave, "NAME", STACK_SIZE, NULL, tskIDLE_PRIORITY, &xHandle);
// ...
// Use the handle to suspend the created task vTaskSuspend(xHandle);
// ...
// Created task will not run during this period
// ...
// Resume the suspended task ourselves.
vTaskResume(xHandle);
}

## Slide 14: taskYield
taskYIELD() is used to request a context switch to another task. However, if there are no other tasks at a higher or equal priority to the task that calls taskYIELD(), then the RTOS scheduler will simply select the task that called taskYIELD() to run again.

## Slide 15: Idle Task Hook
Recall:
  An Idle task is created when vTaskStartScheduler() is called so that there is always at least a task to run
Can add special functionality into the idle task through an idle hook (or call-back) function
  void vApplicationIdleHook(void){...}
  A function that is automatically called by the idle task once per iteration of the idle task loop
Common uses for the Idle task hook include:
  Executing low priority, background or continuous task
  Measuring the amount of spare processing capacity
  Placing the processor into a low power mode
Notes: The idle task will only run when all the other tasks have no work to perform, so measuring the amount of processing time allocated to the idle task provides a clear indication of how much processing time is spare.

## Slide 16: Changing the Priority of a Task
void vTaskPrioritySet(TaskHandle_t pxTask, UBaseType_t uxNewPriority);
  Set the priority of any task
  pxTask: handle of the task whose priority is being modified (NULL for itself)
  uxNewPriority: the priority to which the task is to be set
    Capped to the maximum available priority (configMAX_PRIORITIES – 1), where configMAX_PRIORITIES is a compile time option set in the FreeRTOSConfig.h header file
  A context switch will occur before the function returns if the priority being set is higher than the currently executing task
unsigned portBASE_TYPE uxTaskPriorityGet(xTaskHandle pxTask);

## Slide 17: Sample Code for Changing Priority
void vTask1(void *pvParameters) {
unsigned portBASE_TYPE uxPriority;
uxPriority = uxTaskPriorityGet(NULL); // my priority
for( ;; ) {
Serial.println(“Task1 raises Task2’s priority");
vTaskPrioritySet(xTask2Handle, (uxPriority + 1));
/* For Task1 to reach this point Task2 must
set its priority back down to below Task1. */ }
}
void vTask2(void *pvParameters) {
unsigned portBASE_TYPE uxPriority;
uxPriority = uxTaskPriorityGet(NULL);
for( ;; ) {
vPrintString(“Task2 lower its priority\r\n");
vTaskPrioritySet(NULL, (uxPriority - 2)); }
}

## Slide 18: Sample Code for Changing Priority
xTaskHandle xTask2Handle;
int main(void) { // change to setup() on Arduino
// Create Task1 at priority 2
xTaskCreate(vTask1, "Task 1", 1000, NULL, 2, NULL);
// Create Task2 at priority 1
xTaskCreate(vTask2, "Task 2", 1000, NULL, 1,
&xTask2Handle);
// Start the scheduler
vTaskStartScheduler();
/* If all is well, then main() will never reach here
as the scheduler will now be running the tasks.
If main() does reach here, then it is likely that
there was insufficient heap memory available for
the idle task to be created.*/
for( ;; );
}

## Slide 19: Summary
FreeRTOS runs Fixed Priority Preemptive Scheduling
  Each task is assigned a priority
  Each task can exist in one of several states
  Only one task can exist in Running state at any one time
  The scheduler will always select the highest priority Ready state task to enter the Running state, thus preempting the task that was running before the tick
  Scheduling is made at each tick interrupt
Notes: ‘Fixed Priority’ because each task is assigned a priority that is not altered by the kernel itself (only tasks can change priorities).
‘Preemptive’ because a task entering the Ready state or having its priority altered will always pre-empt the Running state task if the Running state task has a lower priority.

## Slide 20: Outline
Task scheduler of FreeRTOS
  Priority and ticks
  Delaying a task
  Suspending and resuming a task
  Idle task hook
  Changing priority
Representative RT scheduling algorithms
  Rate monotonic, earliest deadline first

## Slide 21: Real-Time Scheduling algorithms
A scheduling algorithm is a scheme that selects what task to run next
  Must be able to meet deadlines in all cases
  Can be preemptive or non-preemptive
  Dynamic or static priorities
Two representative RT scheduling algorithms
  Rate monotonic (RM): static priority, simple to implement, nice properties
  Earliest deadline first (EDF): dynamic priority, harder to implement, very nice properties

## Slide 22: Rate Monotonic Scheduling
RMS [Liu and Layland, 73]: widely-used, analyzable scheduling policy
Assumptions:
  All tasks run periodically on single CPU
  Zero context switch time
  No data dependencies between tasks
  Task execution time is constant
  Deadline is at end of respective period
  Highest-priority ready task runs
  Tasks can be preempted
Liu & Layland, “Scheduling algorithms for multi-programming in a hard-real-time environment”, Journal of ACM, 1973.

## Slide 23: Rate Monotonic Scheduling
Optimal (fixed) priority assignment:
  Shortest-period task gets highest priority, i.e., priority inversely proportional to period; break ties arbitrarily
No fixed-priority scheme does better
  In terms of CPU utilization while ensuring all tasks meet their deadlines
0
5
10
15
Deadline missed!
response time of T3

## Slide 24: RMS Example
Task Execution time Period
P1 1 4
P2 2 6
P3 3 12
time
0
6
2
4
12
8
10
P1
P2
P3
P1
P1
P2
P3
P3
Preempted
Resumed
Preempted
Resumed

## Slide 25: RMS Example
Task Execution time Period
P1 2 4
P2 3 6
P3 3 12
No feasible task assignment to satisfy deadlines:
  In 12 unit intervals, execute P1 3 times, P2 2 times, P3 1 times  (6+6+3)=15 unit intervals
  Let n be # of tasks, if total utilization < n(21/n-1), tasks are schedulable (at n=∞  69.3%)
  This means that RMS algorithm will work if the total CPU utilization is less than 2/3!

## Slide 26: Earliest-Deadline-First Scheduling (EDF)
Task closest to its deadline has highest priority
  Requires recalculating tasks at every time unit
  Dynamic priority assignment: priority of a task is assigned as the task arrives
  Tasks do not have to be periodic
EDF is an optimal uniprocessor scheduling algorithm
  Can use 100% of CPU
  Scheduling cost is high and ready queue can reassign priority
  May fail to meet a deadline
  Cannot guarantee who will miss deadline, but RMS can guarantee that the lowest priority task misses deadline

## Slide 27: Example of EDF Algorithm
T1: period 2; execution time 0.9
T2: period 5; execution time 2.3
10
T2
5
2
4
6
8
T1
T1.1 is 2, T2.1 is 5
Priority: T1>T2
T1.2 is 4, T2.1 is 5
Priority: T1>T2
T1 preempts T2
T1.3 is 6, T2.1 is 5
Priority: T2>T1
At time 4.1, T2.1 completes, T1.3 starts to execute